## Slide 1
Pocket SDR Signal IDs
Ver. 0.9 2024-01-05
Ver. 0.10 2024-01-12

## Slide 2: Pocket SDR Signal IDs (1/3)
GPS [1][2][3] | 1575.42 | L1C/A | Q | -158.5 | BPSK(1) | 1023 | 1.023 | 1 | - | 1 | LNAV | 50 | 50 | - |  | L1CA
 |  | L1P(Y)*1 | I | -161.5 | BPSK(10) | 1week | 10.23 | 1week | - | 1week | LNAV | 50 | 50 | - |  | -
 |  | L1M*3 | I | ? | BOC(10,5) | ? | 5.115 | ? | ? | ? | ? | ? | ? | ? | Block IIR-M~ | -
 |  | L1C-D | I | -163.0 | BOC(1,1) | 10230 | 1.023 | 10 | - | 10 | CNAV-2 | 100 | 50 | BCH,LDPC | GPS III~ | L1CD
 |  | L1C-P | I | -158.25 | TMBOC(6,1,4/33) | 10230 | 1.023 | 10 | 1800 | 18000 | - | - | - | - |  | L1CP
 | 1227.6 | L2C/A | Q | -164.5 | BPSK(1) | 1023 | 1.023 | 1 | - | 1 | LNAV | 50 | 50 | - | Block IIR-M~ | -
 |  | L2P(Y)*1 | I | -164.5/-161.5 | BPSK(10) | 1week | 10.23 | 1week | - | 1week | LNAV | 50 | 50 | - |  | -
 |  | L2M*3 | I | ? | BOC(10,5) | ? | 5.115 | ? | ? | ? | ? | ? | ? | ? | Block IIR-M~ | -
 |  | L2C-M | Q/I | -160.0/ -158.5 | BPSK(1)+TDM | 10230 | 0.5115 | 20 | - | 20 | LNAV | 50 | 50 | - | Block IIR-M~ | -
 |  |  |  |  |  |  |  |  |  |  | CNAV | 50 | 25 | 1/2 |  | L2CM
 |  | L2C-L |  |  | BPSK(1)+TDM | 767250 | 0.5115 | 1500 | - | 1500 | - | - | - | - |  | -
 | 1176.45 | L5-I | I | -157.9/-157.0 | BPSK(10) | 10230 | 10.23 | 1 | 10 (NH) | 10 | CNAV | 100 | 50 | 1/2 | Block IIF~ | L5I
 |  | L5-Q | Q | -157.9/-157.0 | BPSK(10) | 10230 | 10.23 | 1 | 20 (NH) | 20 | - | - | - | - |  | L5Q
GLONASS [4][5][6][7] | 1602.0 + 0.5625K*2 | L1C/A*** | I | -161.0 | BPSK(0.5) | 511 | 0.511 | 1 | - / 2** | 1 / 2** | GLO-STR | 100 | 50 | - |  | G1CA
 |  | L1P | Q | ? | BPSK(5) | 5110000 | 5.11 | 1000 | - | 1000 | ? | ? | ? | - |  | -
 | 1600.995 | L1OCd | Q | ? | BPSK(1)+TDM | 1023 | 0.5115 | 2 | 2 (MC) | 4 | GLO-STR | 250 | 125 | 1/2 | GLO-K2~ | G1OCD
 |  | L1OCp |  |  | BOC(1,1)+TDM | 4092 | 0.5115 | 8 | - | 8 | - | - | - | - |  | G1OCP
 |  | L1SC *4 | I | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? |  | -
 | 1246.0 + 0.4375K*2 | L2C/A*** | I | -167.0 | BPSK(0.5) | 511 | 0.511 | 1 | - / 2** | 1 / 2** | GLO-STR | 100 | 50 | - |  | G2CA
 |  | L2P | Q | ? | BPSK(5) | 5110000 | 5.11 | 1000 | - | 1000 | ? | ? | ? | - |  | -
 | 1248.06 | L2CSI | Q | ? | BPSK(1)+TDM | ? | 0.5115 | ? | ? | ? | ? | ? | ? | ? | GLO-K2~ | -
 |  | L2OCp |  |  | BOC(1,1)+TDM | 10230 | 0.5115 | 20 | 50 | 1000 | - | - | - | - |  | G2OCP
 |  | L2SC *4 | I | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? |  | -
 | 1202.025 | L3OCd | I | ? | BPSK(10) | 10230 | 10.23 | 1 | 5 (BC) | 5 | GLO-STR | 200 | 100 | 1/2 | GLO-K1~ | G3OCD
 |  | L3OCp | Q | ? | BPSK(10) | 10230 | 10.23 | 1 | 10 (NH) | 10 | - | - | - | - |  | G3OCP
Galileo[8] | 1575.42 | E1-A | Q | ? | BOC(15,2.5) | ? | 2.5575 | ? | ? | ? | G/NAV | ? | ? | ? | PRS | -
 |  | E1-B | I | -157.0 | CBOC(6,1,1/11) | 4092 | 1.023 | 4 | - | 4 | I/NAV | 250 | 125 | 1/2 | OS, SoL, CS | E1B
 |  | E1-C | Q |  | CBOC(6,1,1/11) | 4092 | 1.023 | 4 | 25 | 100 | - | - | - | - |  | E1C
 | 1176.45 | E5a-I | I | -155.0 | BPSK(10) | 10230 | 10.23 | 1 | 20 | 20 | F/NAV | 50 | 25 | 1/2 | OS, CS | E5AI
 |  | E5a-Q | Q |  | BPSK(10) | 10230 | 10.23 | 1 | 100 | 100 | - | - | - | - |  | E5AQ
 | 1207.14 | E5b-I | I | -155.0 | BPSK(10) | 10230 | 10.23 | 1 | 4 | 4 | I/NAV | 250 | 125 | 1/2 | OS, SoL, CS | E5BI
 |  | E5b-Q | Q |  | BPSK(10) | 10230 | 10.23 | 1 | 100 | 100 | - | - | - | - |  | E5BQ
*1 AS ON, *2 K = {-7 ... +6}, *3 Military Signal, *4 Secured Service Signal, ** Odd FCN, *** (L1OF), (L2OF)
System | Carrier Freq. (MHz) | Signal | I/Q | Min Rec. Power (dBW) | Modulation | Primary Code |  |  | Overlay Code |  | Navigation Data |  |  |  | Notes | Pocket SDR Signal ID
 |  |  |  |  |  | Length (chip) | Chip Rate (Mcps) | Cycle (ms) | Length (chip) | Cycle (ms) | Data | Symbol Rate (sps) | Data Rate (bps) | FEC |  | 

## Slide 3: Pocket SDR Signal IDs (2/3)
Galileo (Cont.) | 1191.795 | E5a+b*5 | - | (-152.0) | 8-PSK(10) | 10230 | 10.23 | 1 | 100 | 100 | - | - | - | - |  | -
 | 1278.75 | E6-A | Q | ? | BOC(10,5) | ? | 5.115 | ? | ? | ? | G/NAV | ? | ? | ? | PRS | -
 |  | E6-B | I | -155.0 | BPSK(5) | 5115 | 5.115 | 1 | - | 1 | C/NAV | 1000 | 500 | 1/2 | CAS, HAS | E6B
 |  | E6-C | Q |  | BPSK(5) | 5115 | 5.115 | 1 | 100 | 100 | - | - | - | - |  | E6C
QZSS [9][10][11][12] | 1575.42 | L1C/A | I/Q | -158.5*6 | BPSK(1) | 1023 | 1.023 | 1 | - | 1 | LNAV | 50 | 50 | - |  | L1CA
 |  | L1C/B | I | -158.5 | BOC(1,1) | 1023 | 1.023 | 1 | - | 1 | LNAV | 50 | 50 | - |  | L1CB
 |  | L1C-D | I | -163.0*7 | BOC(1,1) | 10230 | 1.023 | 10 | - | 10 | CNAV2 | 100 | 50 | BCH,LDPC |  | L1CD
 |  | L1C-P | Q | -158.25 | BOC(1,1) | 10230 | 1.023 | 10 | 1800 | 18000 | - | - | - | - | Block I | L1CP
 |  |  | I | -158.25*8 | TMBOC(6,1,4/33) | 10230 | 1.023 | 10 | 1800 | 18000 | - | - | - | - | Block II | L1CP
 |  | L1S | I | -161.0/-158.5 | BPSK(1) | 1023 | 1.023 | 1 | - | 1 | L1S | 500 | 250 | 1/2 | SLAS | L1S
 | 1227.6 | L2C-M | I | -160.0/ -158.5 | BPSK(1)+TDM | 10230 | 0.5115 | 20 | - | 20 | CNAV | 50 | 25 | 1/2 |  | L2CM
 |  | L2C-L |  |  | BPSK(1)+TDM | 767250 | 0.5115 | 1500 | - | 1500 | - | - | - | - |  | -
 | 1176.45 | L5-I | I | -157.9/-157.0 | BPSK(10) | 10230 | 10.23 | 1 | 10 (NH) | 10 | CNAV | 100 | 50 | 1/2 |  | L5I
 |  | L5-Q | Q | -157.9/-157.0 | BPSK(10) | 10230 | 10.23 | 1 | 20 (NH) | 20 | - | - | - | - |  | L5Q
 |  | L5S-I | I | -157.0*9 | BPSK(10) | 10230 | 10.23 | 1 | - | 1 | L5S | 500 | 250 | 1/2 | Normal mode | L5SI
 |  |  |  |  |  |  |  |  | 2 (MC) | 2 | L5S | 500 | 250 | 1/2 | Verif. mode | L5SIV
 |  | L5S-Q | Q |  | BPSK(10) | 10230 | 10.23 | 1 | 20 (NH) | 20 | - | - | - | - | Normal mode | L5SQ
 |  |  |  |  |  |  |  |  | 2 (MC) | 2 | - | - | - | - | Verif. mode | L5SQV
 | 1278.75 | L6D | I | -155.7 | BPSK(5)+TDM | 10230 | 2.5575 | 4 | - | 4 | L6D | 2000 | 2000 | RS | CLAS | L6D
 |  | L6L |  |  | BPSK(5)+TDM | 1048575 | 2.5575 | 410 | 2 (MC) | 820 | - | - | - | - | Block I | -
 |  | L6E |  |  | BPSK(5)+TDM | 10230 | 2.5575 | 4 | - | 4 | L6E | 2000 | 2000 | RS | MADOCA-PPP | L6E
BeiDou [13][14][15] [16][17] | 1561.098 | B1I | I | -163.0 | BPSK(2) | 2046 | 2.046 | 1 | 20 (NH) | 20 | D1 | 50 | 50 | BCH |  | B1I
 |  |  |  |  |  |  |  | 1 | - | 1 | D2 | 500 | 500 | BCH | GEO | B1I
 |  | B1Q*10 | Q | ? | BPSK(2) | ? | 2.046 | ? | ? | ? | ? | ? | ? | ? |  | -
 | 1575.42 | B1C-D | I | -159.0/ -161.0 | BOC(1,1) | 10230 | 1.023 | 10 | - | 10 | B-CNAV1 | 100 | 50 | NB-LDPC | BDS-3 | B1CD
 |  | B1C-P | Q |  | QMBOC(6,1,4/33) | 10230 | 1.023 | 10 | 1800 | 18000 | - | - | - | - |  | B1CP
 |  | B1A-D*10 | I | ? | BOC(14,2) | ? | 2.046 | ? | ? | ? | ? | ? | ? | ? |  | -
 |  | B1A-P*10 | Q |  |  | ? | 2.046 | ? | ? | ? | - | - | - | - |  | -
 | 1176.45 | B2a-D | I | -156.0/ -158.0 | BPSK(10) | 10230 | 10.23 | 1 | 5 | 5 | B-CNAV2 | 50 | 25 | NB-LDPC | BDS-3 | B2AD
 |  | B2a-P | Q |  | BPSK(10) | 10230 | 10.23 | 1 | 100 | 100 | - | - | - | - |  | B2AP
 | 1207.14 | B2I | I | ? | BPSK(2) | 2046 | 2.046 | 1 | 20 (NH) | 20 | D1 | 50 | 50 | BCH |  | B2I
 |  |  |  |  |  |  |  | 1 | - | 1 | D2 | 500 | 500 | BCH | GEO | B2I
*5 AltBOC *6 -164.0 dBW (SVID=7), *7 -167.2 dBW (SVID=7), *8 -162.4 dBW (SVID=7), *9 -162.6 dBW (SVID=3), *10 Authorized signal
System | Carrier Freq. (MHz) | Signal | I/Q | Min Rec. Power (dBW) | Modulation | Primary Code |  |  | Overlay Code |  | Navigation Data |  |  |  | Notes | Pocket SDR Signal ID
 |  |  |  |  |  | Length (chip) | Chip Rate (Mcps) | Cycle (ms) | Length (chip) | Cycle (ms) | Data | Symbol Rate (sps) | Data Rate (bps) | FEC |  | 

## Slide 4: Pocket SDR Signal IDs (3/3)
BeiDou (Cont.) | 1207.14 | B2Q*10 | Q | ? | BPSK(10) | 10230 | 10.23 | 1 | ? | ? | ? | ? | ? | ? |  | -
 | 1207.14 | B2b-I | I | -160.0/ -162.0 | BPSK(10) | 10230 | 10.23 | 1 | - | 1 | B-CNAV3 | 1000 | 500 | NB-LDPC | BDS-3 | B2BI
 |  |  |  |  |  |  |  |  |  |  | B2b-PPP | 1000 | 500 | NB-LDPC | BDS-3, GEO | B2BI
 |  | B2b-Q*10 | Q | ? | BPSK(10) | 10230 | 10.23 | 1 | ? | ? | ? | ? | ? | ? | BDS-3 | -
 | 1191.795 | B2a+b*11 | - | ? | 8-PSK(10) | 10230 | 10.23 | 1 | ? | ? | - | - | - | - |  | -
 | 1268.52 | B3I | I | -163.0 | BPSK(10) | 10230 | 10.23 | 1 | 20 (NH) | 20 | D1 | 50 | 50 | BCH |  | B3I
 |  |  |  |  |  |  |  | 1 | - | 1 | D2 | 500 | 500 | BCH | GEO | B3I
 |  | B3Q*10 | Q | ? | BPSK(10) | ? | 10.23 | ? | ? | ? | ? | ? | ? | ? |  | -
 |  | B3A-D*10 | I | ? | BPSK(10) | ? | 10.23 | ? | ? | ? | ? | ? | ? | ? | BDS-3 | -
 |  | B3A-P*10 | Q |  | BPSK(10) | ? | 10.23 | ? | ? | ? | - | - | - | - |  | -
NavIC [18][19] | 1575.42 | L1-SPS-D | Q | -159.6 | BOC(1,1) | 10230 | 1.023 | 10 | - | 10 | IRN-NAV | 100 | 50 | BCH,LDPC | NVS-01~ | I1SD
 |  | L1-SPS-P | I | -158.2 | MBOC(6,1,4/33) | 10230 | 1.023 | 10 | 1800 | 18000 | - | - | - | - |  | I1SP
NavIC [18][19] | 1176.45 | L5-SPS | *12 | -159.0 | BPSK(1) | 1023 | 1.023 | 1 | - | 1 | IRN-NAV | 50 | 25 | 1/2 |  | I5S
 |  | L5-RS-D | *12 | ? | BOC(5,2) | ? | 2.046 | ? | ? | ? | ? | 50 | 25 | 1/2 | *10 | -
 |  | L5-RS-P | *12 | ? | BOC(5,2) | ? | 2.046 | ? | ? | ? | - | - | - | - | *10 | -
 | 2492.028 | S-SPS | *12 | -162.3 | BPSK(1) | 1023 | 1.023 | 1 | - | 1 | IRN-NAV | 50 | 25 | 1/2 |  | ISS
 |  | S-RS-D | *12 | ? | BOC(5,2) | ? | 2.046 | ? | ? | ? | ? | 50 | 25 | 1/2 | *10 | -
 |  | S-RS-P | *12 | ? | BOC(5,2) | ? | 2.046 | ? | ? | ? | - | - | - | - | *10 | -
SBAS | 1575.42 | L1C/A | I | - | BPSK(1) | 1023 | 1.023 | 1 | - | 1 | SBAS | 500 | 250 | 1/2 | PRN120-158 | L1CA
 | 1176.45 | L5-I | I | - | BPSK(10) | 10230 | 10.23 | 1 | 2 (MC) | 2 | L5 SBAS | 500 | 250 | 1/2 | PRN120-158 | L5I
 |  | L5-Q | Q | - | BPSK(10) | 10230 | 10.23 | 1 | 2 (MC) | 2 | - | - | - | - |  | L5Q
[1] IS-GPS-200K, Navstar GPS space segment/navigation user interfaces - interface specification, 2019, [2] IS-GPS-800F, Navstar GPS space segment/user segment L1C interface - interface specification, 2019, [3] IS-GPS-705A, Navstar GPS space segment/user segment L5 interface - interface specification, 2010, [4] GLONASS interface control document - navigation radiosignal in bands L1, L2, version 5.1, 2008, [5] GLONASS interface control document - code division multiple access open service navigation signal in L1 frequency band, edition 1.0, 2016, [6] GLONASS interface control document - code division multiple access open service navigation signal in L2 frequency band, edition 1.0, 2016, [7] GLONASS interface control document - code division multiple access open service navigation signal in L3 frequency band, edition 1.0, 2016, [8] European GNSS (Galileo) open service signal-in-space interface control document (OS SIS ICD), Issue 1, Revision 3, 2016, [9] Quasi-Zenith satellite system interface specification - satellite positioning, navigation and timing service (IS-QZSS-PNT-003), 2018, [10] Quasi-zenith satellite system interface specification - sub-meter level augmentation service (IS-QZSS-L1S-003), 2018, [11] Quasi-zenith satellite system interface specification - centimeter level augmentation service (IS-QZSS-L6-003), 2018, [12] Quasi-zenith satellite system interface specification - positioning technology verification service (IS-QZSS-TV-004), 2023, [13] BeiDou navigation satellite system signal in space interface control document - open service signal B1I, version 3, 2019, [14] BeiDou navigation satellite system signal in space interface control document - open service signal B1C, version 1.0, 2017, [15] BeiDou navigation satellite system signal in space interface control document - open service signal B2a, version 1.0, 2017, [16] BeiDou navigation satellite system signal in space interface control document - open service signal B3I, version 1.0, 2018, [17] BeiDou navigation satellite system signal in space interface control document - Precise Point Positioning service signal PPP-B2b, version 1.0, 2020, [18] Indian Regional Navigation Satellite System, Signal in space ICD for standard positioning service version 1.1, 2017, [19] NAVIC signal in space ICD for standard positioning service in L1 frequency version 1.0, 2023
*10 Authorized signal, *11 ACE-BOC, *12 Interplex Modulation
System | Carrier Freq. (MHz) | Signal | I/Q | Min Rec. Power (dBW) | Modulation | Primary Code |  |  | Overlay Code |  | Navigation Data |  |  |  | Notes | Pocket SDR Signal ID
 |  |  |  |  |  | Length (chip) | Chip Rate (Mcps) | Cycle (ms) | Length (chip) | Cycle (ms) | Data | Symbol Rate (sps) | Data Rate (bps) | FEC |  |